Background Generator

The background layer shows when there is nothing to display from the layers above. There are 16 named background generators in libPAWS. The result of the individual background generators are shown in the table below.

Result of set_background( PURPLE, ORANGE, value from table );
BKG_SOLID	BKG_5050_V	BKG_5050_H	BKG_CHKBRD_5
BKG_RAINBOW	BKG_SNOW	BKG_STATIC	BKG_CHKBRD_1
BKG_CHKBRD_2	BKG_CHKBRD_3	BKG_CHKBRD_4	BKG_HATCH
BKG_LSLOPE	BKG_RSLOPE	BKG_VSTRIPE	BKG_HSTRIPE

In addition, a simple co-processor, called COPPER, is available to change background generator parameters during the frame generation.
Background COPPER Programming (New Copper NuCu)

The COPPER is designed to allow the changing of the background generator parameters during the display frame., referred to as NuCU.

NuCu has a fixed instruction set, with 4 fields as detailed below.

OPCODE	DEST REG AND REG1	REG2 REG / LITERAL FLAG	REG2 / LITERAL	EXAMPLE	MEANING
CU_JMP		Y	Y	JMP 7	JUMP to RL
CU_SET	Y	Y	Y	SET R1 ← (R0)	SET register to RL
CU_ADD	Y	Y	Y	ADD R0 ← (R0) + 1	ADD RL to (reg1) store in reg1
CU_SUB	Y	Y	Y	SUB R0 ← (R0) - 1	SUB RL from (reg1) store in reg1
CU_AND	Y	Y	Y	AND R0 ← (R0) & 7	AND (reg1) by RL store in reg1
CU_OR	Y	Y	Y	OR R0 ← (R0) | 1	OR (reg1) by RL store in reg1
CU_XOR	Y	Y	Y	XOR R0 ← (R0) ^ 1	XOR (reg1) by RL store in reg1
CU_SHL	Y	Y	Y	SHL (R0) ← (R0) << 6	Shift Left (reg1) by RL store in reg1
CU_SHR	Y	Y	Y	SHR (R0) ← (R0) >> 1	Shift Right (reg1) by RL store in reg1
CU_SEQ	Y	Y	Y	SEQ (R0) == (Y)	Skip next if (reg1) == RL
CU_SNE	Y	Y	Y	SNE (R0) == (X)	Skip next if (reg1) != RL
CU_SLT	Y	Y	Y	SLT (R0) < (R1)	Skip next if (reg1) < RL
CU_SLE	Y	Y	Y	SLE (R0) <= (R1)	Skip next if (reg1) <= RL
CU_RND	Y	Y	Y
CU_LFM	Y	Y	Y
CU_STM	Y	Y	Y
(reg) refers to value of the register. [ addr ] refers directly to contents of a memory cell. [ (reg) ] refers to the cotents of a memory cell identified by the value of the register. RL refers to (reg2) or literal value depending on the register/literal flag

NuCu has program storage for 128 entries.

A simple COPPER program that sets the background generator to the BKG_SNOW pattern on a BLACK background, and changes the colour of the snow/stars every 64 pixels down the screen to give a rainbow effect.
copper_startstop( 0 ); / unsigned short memoryinit[8] = { / WHITE, / RED, / ORANGE, / YELLOW, / GREEN, / LTBLUE, / PURPLE, / MAGENTA / }; / copper_set_memory( memoryinit ); // PROGRAM COPPER MEMORY ARRAY OF COLOURS / copper_program( 0, CU_SET, CU_BM, CU_RL, BKG_SNOW ); // BACKGROUND SNOW GENERATOR / copper_program( 1, CU_SET, CU_BA, CU_RL, BLACK ); // BACKGROUND ALT BLACK / copper_program( 2, CU_SET, CU_BC, CU_RL, WHITE ); // BACKGROUND WHITE / copper_program( 3, CU_SET, CU_R0, CU_RL, 0 ); // SET R0 = 0 / copper_program( 4, CU_SET, CU_R1, CU_RR, CU_R0 ); // SET R1 = R0 / copper_program( 5, CU_SHL, CU_R1, CU_RL, 6 ); // R1 = R1 * 64 / copper_program( 6, CU_LFM, CU_R2, CU_RR, CU_R0 ); // R2 = MEM[ R0 ] / copper_program( 7, CU_SEQ, CU_RY, CU_RR, CU_R1 ); // Y == R1 ? / copper_program( 8, CU_JMP, FALSE, CU_RL, 7 ); // SKIP YES, ELSE GO TO 7 / copper_program( 9, CU_SET, CU_BC, CU_RR, CU_R2 ); // SET BACKGROUND = R2 / copper_program( 10, CU_ADD, CU_R0, CU_RL, 1 ); // R0 = R0 + 1 / copper_program( 11, CU_AND, CU_R0, CU_RL, 7 ); // R0 = R0 & 7 / copper_program( 12, CU_JMP, FALSE, CU_RL, 4 ); // JUMP 4 / copper_startstop( 1 );